Product Data Sheet

MSHS-205

MSHS-205 is a single pack, multi-functional liquid, designed & developed according to the specific conditions of water in Open Evaporative Humidifier.

Humidifying Water Circuit provides excellent atmosphere for the growth of problems, such as Scale & Corrosion. MSHS-205  combat all these conditions.

It offers excellent Scale & Corrosion inhibition for Ferrous/Non-Ferrous metals and their alloys. It is 100% compatible with a wide range materials

SPECIFICATIONS:

Appearance			:		Brownish Liquid

pH				:		0.5 – 1.5

Solubility in Water		:		Completely miscible.

Specific Gravity			:		Approx. 1.2 at 20oC

APPLICATION AND DOSAGE:

MSHS-205 should be fed into the feed water line or to the sump of the humidifier.

A recommended Zinc level must be maintained in Circulating Water.

PRECAUTIONS:

MSHS-205 should not be used in water intended for human consumption.

MSHS-205 must be handled with proper safety precautions. For open handling, person should be equipped with rubber gloves, aprons and goggles. Harmful if swallowed. May cause irritation to skin and eyes. Avoid contact with skin, eyes and clothing. Wash thoroughly after handling. Wash empty drums before dispose off. Store in a cool & dry place.

FIRST AID :

In case of contact, immediately flush with plenty of water for at least 5 minutes. If swallowed, promptly drink large quantity of water.

PACKAGING:

MSHS-205 is available in 35 and 100 Kg  packing.